Conjoint Vehicle License Plate Identification System

Yair Wiseman

Bar-Ilan University

wiseman@cs.biu.ac.il

Abstract: Autonomous vehicle will go unaccompanied to park themselves in a remote parking lot without a driver or a passenger inside. In order to avoid mistakes in identification of the vehicle by the automatic identification device, it is proposed to back up license plates identification procedure by making use of three distinct identification techniques: RFID, Bluetooth and OCR with the aim of making identification mistakes hardly ever happen.

Keywords: Autonomous Vehicle, Automatic Identification, Parking, State Machine

1. Introduction

Hectic parking lots are a notorious nuisance for many people living in urban areas []. Autonomous vehicles will be capable to put an end to this nuisance [,], by sending out the autonomous vehicles to park in remote parking lots and freeing the hectic parking lots nearby crowded sites [] .

It has been noted in [] that approximately a third of central regions in main cities in the United States are used for parking. Autonomous vehicle will be able to bring about a replacement of the land uses in metropolitan areas anyplace by switching large parking lots into various alternative usages

Autonomous vehicles will be able to improve on several parking concerns because of three key reasons:

- While traditional vehicles require an adjacent parking, autonomous vehicles will be able to drop passengers off in wherever a road is present. Moreover, as opposed to traditional vehicles that frequently cruise for parking [], autonomous vehicles will be able to park themselves in a remote site in a rural fringe of any city where inexpensive land is typically more readily available.

- Autonomous vehicles are able to park in a tighter parking slot without taking the risk of scratching nearby vehicles. Furthermore, if a human driver parks a vehicle, he will need some space to be able to open the vehicle door and walk away; however, autonomous vehicles do not need any space, because no one needs to get out and walk away from the vehicle. In addition, parking lots of autonomous vehicles will not require elevators nor will they need staircases. Therefore, a larger number of autonomous vehicles compared to traditional vehicles are able to park in a parking lot of the same size. There are different analyses of how much space can be reduced in autonomous vehicle parking lots. While in [] the authors evaluate the influence of the dense parking of autonomous vehicles in an averagely reduction of 15% of the parking lot size, the authors of [] evaluate that parking lots of autonomous vehicles will be able to accommodate more cars in the region of 62% to 87% than parking lots for traditional vehicles.

- A computerized decision will determine the exact position for parking of the autonomous vehicles [], therefore all the vehicles will park in a strict order with no angles that cause disorganized parking.

Therefore, autonomous vehicles will be sent out to remote sites for parking. When the autonomous vehicle is needed by a user, he will call the vehicle and the vehicle will come by itself to pick up the user.

Parking autonomous vehicles in a farer parking lot can raise objections because residents of the rural fringes might be unhappy with new unwelcomed traffic of autonomous vehicles drive to their reserved parking lot.

The parking lot service provider also has concerns. There is a cost for constructing and maintaining a reserved parking lot for autonomous vehicles. Although land price in rural fringe is much cheaper than in the urban core, the land is still obviously not for free and as was pointed out in [], remote parking cannot be in nowhere, but rather in a distance of less than 10 miles; otherwise, the user of the autonomous vehicle will not send out the vehicle to park itself in this autonomous vehicle parking lot, because it will be tiresome to wait a long time until the vehicle gets back and pick him up.

For that reasons, the neighbors and the owner of the parking lots aim at developing an automatic gatekeeper that lets only authorized vehicles entering the reserved parking lot for autonomous vehicles.

1. License Plate Identification

In a dedicated parking lot for autonomous vehicles the necessity of an automated system in the arriving and leaving vehicles for an automated fee collection will be crucial. Many autonomous vehicles will arrive empty at the parking lot with neither a driver, nor a passenger. The autonomous vehicles will be able to drive by themselves to the parking lot and there will be no one to talk to in the vehicle. Also a gatekeeper is unnecessary because an automated system can charge the fee.

We implemented a conjoint identification method making use of three common practices for vehicle identification:

- RFID (Radio Frequency Identification) device that without human intervention is able to identify tags attached to vehicles by making use of electromagnetic fields [].

- Bluetooth device that makes use of UHF radio waves for exchanging information over short distance between a vehicle and a device attached to the parking lot gateway [].

- OCR (Optical Character Recognition) device that is able to identify vehicles by reading their license plates and understand the numbers by image processing techniques [].

Figure 1. The three techniques used to identify vehicles - RFID tag on a vehicle, Bluetooth equipment and OCR Camera.

The three practices are essential because errors sometimes can happen – a vehicle can be mistakenly identified as a different vehicle or a vehicle cannot be identified at all. If such identification incidents happen, the parking lot operator might have a loss. Furthermore, if a different vehicle is mistakenly identified, the owner or the lessee of the different vehicle will be required to go to the trouble of proving that he does not have to pay the wrong demand for payment.

Figure 1 shows the techniques used in the conjoint vehicle license plate identification system.

2. Putting into Practice the Conjoint System

Intelligent Transportation Systems for the most part are implemented using state machines and the suggested conjoint license plate identification system of this paper is no exception. The state machine of the conjoint license plate identification system is in charge of deciding which identification device out of OCR, RFID and Bluetooth is correct when a conflict occurs.

In the capacity of efficient data transmission, RFID is the most reliable technique [,,]. RFID averagely has a low error bit rate of typically less than 0.01% []. Bluetooth is less reliable than RFID as it has a typically error bit rate of 0.1% [], whereas OCR is the least reliable technique as it has an error bit rate of 3.6% [] which is the highest error bit rate of the three techniques we use.

The state machine in the conjoint license plate identification system decides which output out of the three techniques' output will be sent as the correct license plate number. Since the RFID and the Bluetooth have a better error bit rate, the system first of all looks at their output. Only if the outputs of the RFID device and the Bluetooth device are not the same, the output of the OCR device will be examined. The state machine for the conjoint license plate identification system is depicted in Figure 2.

Figure 2. State machine for the conjoint license plate identification system

Specifically, the conjoint license plate identification system algorithm is:

- Obtain the outputs of the RFID device and the Bluetooth device.

  - We use an implementation of 0.5MHz clock rate [], but the Bluetooth device is not able to produce the output so fast. In fact, it takes the Bluetooth device to produce the output approximately 7.38μs. Accordingly, the state machine has four "get" states with the purpose of synchronized output producing. Four states take 8μs which is more than the 7.38μs required for the Bluetooth device to produce the output. There are other faster Bluetooth devices and if a system uses one of these faster Bluetooth devices, the number of the "get" states can be reduced into a smaller number than four.

- The output of the RFID device and the output of the Bluetooth device are compared to verify they are equal.

  - Usual comparator circuits [] can also detect which number is greater and which number smaller; however, we use a simple comparator that only gives a Boolean answer whether the outputs are equal or not. The simple comparator is depicted in Figure 3:

Figure 3. Comparator between the outputs

- If the comparator finds that the RFID output and the Bluetooth output are equal, no further check will be done and the RFID output is taken as the correct license plate number. As was mentioned above, the RFID device and the Bluetooth device are more accurate than the OCR device, so even if the output of the OCR device is different, it will be discarded.

- Else, there is a mistake either in the RFID device or the Bluetooth device. Our policy to realize which device has a mistake is by checking the output of the OCR device. The device that produces the same output as OCR device produces is assumed to have the correct output.

  - The OCR device is much slower, specifically producing the output in our OCR device takes 21.42μs, therefore the system requires eleven cycles; however, the system activates the OCR device in the beginning along with the activation of the RFID device and the Bluetooth device. If the system finds after four cycles that the RFID device and the Bluetooth device give the same output and the OCR output is no longer needed, the OCR device can be discontinued. Nevertheless, if the RFID device and the Bluetooth device give different outputs and the OCR device is needed for the final resolution, the system will wait only seven more cycles besides of the four cycles that the system has already waited for the Bluetooth device and therefore there is no need for dedicated eleven states for the waiting for the OCR device.

- If the three different devices produce three different outputs, the system will take the output of the RFID device as the correct license plate number. As was mentioned above, the RFID device is the most reliable device, so the system prefers its output. Only if both the Bluetooth device and the OCR device agree on a license plate number, the system will take the output of the Bluetooth device and the OCR device as the correct output.

3. Implementation of the Outputs

The conjoint license plate identification system has a number of output bits:

- Decision bit which indicates whether the system finished the operation and has reached to a conclusion what the license number is and the output bits contain the data and can be read. When the system reaches to a conclusion what the license number is this bit will be 1; otherwise it will be 0.

- Enable bits for the RFID output and the Bluetooth output. Only the output of one device should be transmitted. The enable bits decide which output should be forwarded. When the decision bit indicates that the operation of the system has not been completed yet, the values of the enable bits are "don't care" because the enable bits are not read in this phase. Just when the decision bit indicates that the operation of the system is completed, the enable bits will set their values. The enable bit of the selected device will be set to one, whereas the other bit will be set to zero. Just the RFID device and the Bluetooth device have an enable bit. The OCR device does not need an enable bit because its output is never taken. The OCR output will be needed only when a selection between the RFID output and the Bluetooth output is required. If the OCR output is equal to one of them, the correct number is anyway available in the other device. If the OCR output is not equal to the RFID output, nor is it equal to the Bluetooth output, the RFID output will be taken. Therefore, the OCR output is actually never taken and no enable bit is needed for it.

- Output bits which contain the actual value of the license plate number of the vehicle that enters the parking lot.

As was explained above the conjoint license plate identification system has a state machine with 12 states, so the implementation of state machine is by 4 Flip-Flops that represent the binary values of 0000 to 1011. We will denote these Flip-Flops as FF3, FF2, FF1, FF0 where FF3 is the most significant bit and FF0 is the least significant bit.

Figure 4. Karnaugh map for the decision bit

The values of the decision bit are detailed in the Karnaugh map [] in Figure 4 which yields the function:

Decision bit = FF2(FF1'(FF0'+FF3(FF1(FF0

Accordingly, the circuit of the decision bit is depicted in Figure 5.

Figure 5. Implementation of the decision bit

The RFID enable bit and the Bluetooth enable bit can be also obtained from this Karnaugh map because the RFID enable bit function is the left group containing cells 0100 and cell 1100, whereas the Bluetooth enable bit function is the right group containing cells 1011 and cell 1111. Accordingly, the enable bits function are:

RFID enable bit = FF2(FF1'(FF0'

Bluetooth enable bit = FF3(FF1(FF0

Therefore, the circuit of the enable bits is very similar to the circuit of the decision bit as it depicted in Figure 6. As was mentioned above no enable bit is needed for the OCR as its output is never taken.

Figure 6. Implementation of the enable bits

4. Implementation of the Next State Functions

Since the conjoint license plate identification system is comprised of 12 states, so it should contain (Log212( Flip-Flops which are (3.5849625( i.e. four Flip-Flops. Therefore, this system has four next state functions – one function for each of the Flip-Flops. Similarly to the output bits, Karnaugh maps have been used to get the minimal functions for implementing of the next state circuits. We also have chosen to use Edge-Triggered D-Filp-Flops [,] with the aim of a straightforward implementation.

The Karnaugh map of the most significantly bit namely FF3 is shown in Figure 7. States number 12 to number 15 do not exist, so they denoted as "don't care" with the letter X. The next state of state number 10 is depended on the comparison of the OCR output and the Bluetooth output. If these outputs are equal, the next state will be state number 11, where F3 is 1; otherwise the next state will be state number 4, where F3 is 0, so state number 10 was marked as 0 and the condition of OCR=Bluetooth was added to the final function after extracting this function from the Karnaugh map. Therefore, the final next state function for F3 is:

NextFF3=FF3(FF1'+FF3(FF2(FF1+FF3(FF2'(FF1(FF0'(OeB

Where OeB stands for the Boolean condition of whether the OCR output is equal to the Bluetooth output.

Figure 7. Karnaugh map for the next state of FF3

Accordingly, the logic circuit for the next state of FF3 is depicted in Figure 8.

Figure 8. Logic circuit for the next state of FF3

Figure 9. Karnaugh map for the next state of FF2

Similarly to FF3, in the Karnaugh map of FF2, states number 12 to number 15 do not exist, so they denoted as "don't care" with the letter X and the next state of state number 10 is depended on the comparison of the OCR output and the Bluetooth output; however, unlike FF3, in the function of FF2, the next value will be 1 if OCR≠Bluetooth. Therefore, the final next state function for F2 is:

NextFF2=FF2(FF1'(FF0+FF3'(FF2'(FF1(FF0+FF2(FF1(FF0'+FF3(FF2'(FF1(FF0'(OeB'

Figure 10. Logic circuit for the next state of FF2

The Karnaugh map of FF2 is shown in Figure 9, whereas the logic circuit for the next state of FF2 is depicted in Figure 10.

FF1 is not different from FF3 and FF2. Therefore, the "don't care" states and state number 10 are handled in the same way. The Karnaugh map of FF1 is shown in Figure 11 and the function for FF1 is:

NextFF1=FF1'(FF0+FF3'(FF1(FF0'+FF3(FF2'(FF1(FF0'(OeB

Figure 11. Karnaugh map for the next state of FF1

Therefore, the logic circuit for the next state of FF1 is as shown in Figure 12.

Figure 12. Logic circuit for the next state of FF1

The least significant bit is NextFF0 which like FF3, FF2 and FF1 handles the "don't care" states and state number 10 in the same way. Nevertheless, the next state of state number 3 is depended on the comparison of the RFID output and the Bluetooth output, so state number 3 was marked as 0 and the condition of RFID=Bluetooth was added to the final function after extracting this function from the Karnaugh map. Therefore, the final next state function for F0 is:

NextF0=FF2'(FF1'(FF0'+FF3'(FF1(FF0'+FF3'(FF2'(FF1(FF0(ReB+FF3(FF2'(FF1(FF0'(OeB

Where ReB stands for the Boolean condition of whether the RFID output is equal to the Bluetooth output. The Karnaugh map of FF0 is shown in Figure 13, whereas the logic circuit for the next state of FF0 is shown in Figure 14.

Figure 13. Karnaugh map for the next state of FF0

Figure 14. Logic circuit for the next state of FF0

5. Conclusions

Parking lots for autonomous vehicle will be of low cost [,]. The parking lot will be in a remote location where the lands are inexpensive. In addition, autonomous vehicle will be able to park very close to the adjacent vehicle and will park completely straight, so their parking lots will be very efficient and low-priced.

The critical difficulty is to automatically make sure that the autonomous vehicle is correctly identified in the gate, because the vehicle will be unoccupied so no one can be of assistance for the gatekeeper.

The conjoint vehicle license plate identification system can ensure a high level of reliability by identifying the vehicle in three different techniques: RFID, Bluetooth and OCR with the purpose of getting the most trustworthy identification.

6. References

# Endnotes

. O. Kim, T. Thi, N. H. Tran, C. Pham, T. LeAnh, M. T. Thai and C. S. Hong, "Parking Assignment: Minimizing Parking Expenses and Balancing Parking Demand Among Multiple Parking Lots", IEEE Transactions on Automation Science and Engineering, 2019, pp. 1-12.

. Y. Wiseman, "Remote Parking for Autonomous Vehicles", International Journal of Hybrid Information Technology, 2017, Vol. 10(1), pp. 313-324.

. Y. Wiseman, "Self-Driving Car - A Computer will Park for You", International Journal of Engineering & Technology for Automobile Security, 2017, Vol. 1(1), pp. 9-16.

. J. A. Brett, "Thinking Local about Self-Driving Cars: A Local Framework for Autonomous Vehicle Development in the United States", MSc Thesis, University of Washington, 2016.

. D. C. Shoup, "The high cost of free parking", Chicago: Planners Press, 2005.

. A. Millard-Ball, R. C. Hampshire and R. Weinberger, "Parking behaviour: The curious lack of cruising for parking in San Francisco", Land Use Policy, 2020, Vol. 91, Paper No. 103918.

. M. Bertoncello and D. Wee, "Ten ways autonomous driving could redefine the automotive world", McKinsey & Company, June 2015.

. A. Millard-Ball, "The Autonomous Vehicle Parking Problem", Transport Policy, Elsevier, 2019, Vol. 75, pp. 99-108.

. M. Nourinejad, S. Bahrami, and M. J. Roorda, "Designing parking facilities for autonomous vehicles", Transportation Research Part B: Methodological, 2018, Vol. 109, pp. 110-127..

. J. B. Acker, R. N. Cancro and D. J. Pedley, "Location based parking management system", U.S. Patent Application 13/723,056, filed December 20, 2012.

. A. J. Samuel and S. Sebastian, "An algorithm for IoT based vehicle verification system using RFID", International Journal of Electrical & Computer Engineering, Institute of Advanced Engineering & Science, 2019, Vol. 9, No. 5, Part 1, p3751-3758.

. K. Marso and D. Macko, "A New Parking-Space Detection System Using Prototyping Devices and Bluetooth Low Energy Communication", International Journal of Engineering and Technology Innovation, 2019, Vol. 9, No. 2.

. A. Mani and N. J. Panicker, "An Efficient Method for License Plate Detection and Recognition using OCR", 2019, International Journal of Scientific Research in Computer Science, Engineering and Information Technology, Vol. 5, No. 3, pp. 540-547.

. Y. Wiseman, "Compaction of RFID Devices using Data Compression", IEEE Journal of Radio Frequency Identification, 2017, Vol. 1, No. 3, pp. 202-207.

. Y. Wiseman, "Efficient RFID Devices", In Proceedings of The 42nd IEEE Annual Conference of Industrial Electronics Society (IECON 2016), Fortezza da Basso, Firenze (Florence), Italy, 2016, pp. 4762-4766.

. Y. Wiseman, "Compression Scheme for RFID Equipment", In Proceedings of The IEEE International Conference on Electro Information Technology (EIT 2016), Grand Forks, North Dakota, USA, 2016, pp. 387-392.

. G. Fritz, V. Beroulle, M. D. Nguyen, O. Aktouf and I. Parissis, "Read-Error-Rate evaluation for RFID system on-line testing", In proceedings of 16th IEEE International Mixed-Signals, Sensors and Systems Test Workshop (IMS3TW), La Grande Motte, France, 2010, pp. 1-6.

. C. Gomez, J. Oller and J. Paradells, "Overview and Evaluation of Bluetooth Low Energy: An Emerging Low-Power Wireless Technology", Sensors Journal, MDPI, Basel, Switzerland, 2012, Vol. 12, No. 9, pp. 11734-11753.

. L. Zheng, X He, B. Samali and L. T. Yang, "An Algorithm for Accuracy Enhancement of License Plate Recognition", Journal of Computer and System Sciences, Elsevier, March 1, 2013, Vol. 79, No. 2, pp. 245-255.

. M. S. McCorquodale, S. M. Pernia, J. D. O'Day, G. Carichner, E. Marsman, N. Nguyen, S. Kubba, S. Nguyen, J. Kuhn and R. B. Brown, "A 0.5-to-480MHz Self-Referenced CMOS Clock Generator with 90ppm Total Frequency Error and Spread-Spectrum Capability", In proceedings of 2008 IEEE International Solid-State Circuits Conference, (ISSCC), Digest of Technical Papers, San Francisco, CA, USA, 2008, pp. 350-619.

. J. Y. Kim, and H.J. Yoo, "Bitwise competition logic for compact digital comparator", In proceedings of IEEE Asian Solid-State Circuits Conference, 2007, pp. 59-62.

. C. Wang and Y. Tao, "Karnaugh Maps of Logical Systems and Applications in Digital Circuit Design", Circuits, Systems and Signal Processing, 2019, pp. 1-27.

. A. Mall, S. Khanna and A. Noor, "Design of Low-Power Dual Edge-Triggered Retention Flip-Flop for IoT Devices", In Proceedings of International Conference on Recent Innovations in Computing (ICRIC), 2020, Springer, pp. 841-852.

. C. Y. Kim and H. C. Lee, "Low-Power, High-Sensitivity Readout Integrated Circuit With Clock-Gating, Double-Edge-Triggered Flip-Flop for Mid-Wavelength Infrared Focal-Plane Arrays", IEEE Sensors Letters, 2019, Vol. 3, No. 9, pp. 1-4.

. O. O. Olakanmi, "SAPMS: A Secure and Anonymous Parking Management System for Autonomous Vehicles", International Journal of Information and Computer Security, Inderscience, 2020, Vol. 12, No. 1, pp. 20-39.

. K. M. Gurumurthy and K. M. Kockelman, "Modeling Americans’ Autonomous Vehicle Preferences: A Focus on Dynamic Ride-Sharing, Privacy & Long-Distance Mode Choices", Journal of Technological Forecasting and Social Change, Elsevier Inc., 2020, Vol. 150, paper no. 119792.

27. R. B. Yehezkael, Y. Wiseman, H. G. Mendelbaum and I. L. Gordin, "E1periments in Separating Computational Algorithm from Program Distribution and Communication", LNCS of Springer Verlag Vol. 1947, pp. 268-278, 2001.

28. Y. Wiseman, "A Pipeline Chip for Quasi Arithmetic Coding", IEICE Journal - Trans. Fundamentals, Tokyo, Japan, Vol. E84-A(4), pp. 1034-1041, 2001.

29. E. Fredj and Y. Wiseman, "An O(n) Algorithm for Edge Detection in Photos Compressed by JPEG Format", Proc. IASTED International Conference on Signal and Image Processing SIP-2001, Honolulu, Hawaii, pp. 304-308, 2001.

30. Y. Wiseman and E. Fredj, "Contour E4traction of Compressed JPEG Images", ACM - Journal of Graphic Tools, Vol. 6(3), pp. 37-43, 2001.

31. Y. Wiseman, K. Schwan and P. Widener, "Efficient End to End Data E5change Using Configurable Compression", Proc. The 24th IEEE Conference on Distributed Computing Systems (ICDCS 2004), Tokyo, Japan, pp. 228-235, 2004.

32. Y. Wiseman, "ARC Based SuperPaging", Operating Systems Review, Vol. 39(2), pp. 74-78, 2005.

33. Y. Wiseman, "Advanced Non-Distributed Operating Systems Course", ACM - Computer Science Education, Vol. 37(2), pp. 65-69, 2005.

34. M. Reuven and Y. Wiseman, "Reducing the Thrashing Effect Using Bin Packing", Proc. IASTED Modeling, Simulation, and Optimization Conference, MSO-2005, Oranjestad, Aruba, pp. 5-10, 2005.

35. M. Reuven and Y. Wiseman, "Medium-Term Scheduler as a Solution for the Thrashing Effect", The Computer Journal, O9ford University Press, Swindon, UK, Vol. 49(3), pp. 297-309, 2006.

36. Y. Wiseman, "The Relative Efficiency of LZW and LZSS", Data Science Journal, Vol. 6, pp. 1-6, 2007.

37. Y. Wiseman and I. Gefner, "Conjugation Based Compression for Hebrew Te11ts", ACM Transactions on Asian Language Information Processing, Vol .6(1), article no. 4, 2007.

38. Y. Wiseman, "Burrows-Wheeler Based JPEG", Data Science Journal, Vol. 6, pp. 19-27, 2007.

39. I. Grinberg and Y. Wiseman, "Scalable Parallel Collision Detection Simulation", Proc. Signal and Image Processing (SIP-2007), Honolulu, Hawaii, pp. 380-385, 2007.

40. Y. Wiseman, "ASOSI: Asymmetric Operating System Infrastructure", Proc. 21st Conference on Parallel and Distributed Computing and Communication Systems, (PDCCS 2008), New Orleans, Louisiana, pp. 193-198, 2008.

41. Y. Wiseman, J. Isaacson and E. Lubovsky, "Eliminating the Threat of Kernel Stack Overflows", Proc. IEEE Conference on Information Reuse and Integration (IEEE IRI-2008), Las Vegas, Nevada, pp. 116-121, 2008.

42. M. Itshak and Y. Wiseman, "AMSQM: Adaptive Multiple SuperPage Queue Management", Proc. IEEE Conference on Information Reuse and Integration (IEEE IRI-2008), Las Vegas, Nevada, pp. 52-57, 2008.

43. P. Weisberg and Y. Wiseman, "Using 4KB Page Size for Virtual Memory is Obsolete", Proc. IEEE Conference on Information Reuse and Integration (IEEE IRI-2009), Las Vegas, Nevada, pp. 262-265, 2009.

44. Y. Wiseman, "Take a Picture of Your Tire!", Proc. IEEE Conference on Vehicular Electronics and Safety (IEEE ICVES-2010) Qingdao, ShanDong, China, pp. 151-156, 2010.

45. R. Ben Yehuda and Y. Wiseman, "The Offline Scheduler for Embedded Transportation Systems", Proc. IEEE Conference on Industrial Electronics (IEEE ICIT-2011), Auburn, Alabama, pp. 449-454, 2011.

46. D. Livshits and Y. Wiseman, "Cache Based Dynamic Memory Management For GPS", Proc. IEEE Conference on Industrial Electronics (IEEE ICIT-2011), Auburn, Alabama, pp. 441-446, 2011.

47. Y. Wiseman, "The Effectiveness of JPEG Images Produced By a Standard Digital Camera to Detect Damaged Tyres", World Review of Intermodal Transportation Research, Vol. 4(1), pp. 23-36, 2013.

48. Y. Wiseman and P. Weisberg, "Economical Memory Management for Avionics Systems", IEEE/AIAA 31st Digital Avionics Systems Conference (DASC), 2013.

49. Y. Wiseman and A. Barkai, "Diminishing Flight Data Recorder Size", IEEE/AIAA 31st Digital Avionics Systems Conference (DASC), 2013.

50. R. Ben Yehuda and Y. Wiseman, "The Offline Scheduler for Embedded Vehicular Systems", International Journal of Vehicle Information and Communication Systems, Vol. 3(1), pp. 44-57, 2013.

51. D. Livshits and Y. Wiseman, "The Ne26t Generation GPS Memory Management", International Journal of Vehicle Information and Communication Systems, Vol. 3(1), pp. 58-70, 2013.

52. Y. Wiseman, "Fuselage Damage Locator System", Advanced Science and Technology Letters, Vol. 37, pp. 1-4, 2013.

53. I. Grinberg and Y. Wiseman, "Scalable Parallel Simulator for Vehicular Collision Detection", International Journal of Vehicle Systems Modelling and Testing, Vol. 8(2), pp. 119-144, 2013.

54. Y. Wiseman and A. Barkai, "Smaller Flight Data Recorders", Journal of Aviation Technology and Engineering, Vol. 2(2), pp. 45-55, 2013.

55. Y. Wiseman, "Camera That Takes Pictures of Aircraft and Ground Vehicle Tires Can Save Lives", Journal of Electronic Imaging, Vol. 22(4), 041104, 2013.

56. P. Weisberg and Y. Wiseman, "Efficient Memory Control for Avionics and Embedded Systems", International Journal of Embedded Systems, Vol. 5(4), pp. 225-238, 2013.

57. Y. Wiseman, "Steganography Based Seaport Security Communication System", Advanced Science and Technology Letters, Vol. 46, pp. 302-306, 2014.

58. Y. Wiseman, "Device for Detection of Fuselage Defective Parts", Information Journal, Tokyo, Japan, Vol. 17(9(A)), pp. 4189-4194, 2014.

59. P. Weisberg, Y. Wiseman and J. Isaacson, "Enhancing Transportation System Networks Reliability by Securer Operating System", Open Journal of Information Security and Applications, Vol. 1(1), pp. 24-33, 2014.

60. Y. Wiseman, "Noise Abatement at Ben-Gurion International Airport", Advanced Science and Technology Letters, Vol. 67, pp. 84-87, 2014.

61. Y. Wiseman, "The still image lossy compression standard ▒~@~S JPEG", Encyclopedia of Information and Science Technology, Third Edition, Vol. 1, Chapter 28, pp. 295-305, 2014.

62. Y. Wiseman, "Protecting Seaport Communication System by Steganography Based Procedures", International Journal of Security and Its Applications, Sandy Bay, Tasmania, Australia, Vol. 8(4), pp. 25-36, 2014.

63. Y. Wiseman, "Noise Abatement Solutions for Ben-Gurion International Airport", International Journal of U- and E-Service, Science and Technology, Vol. 7(6), pp. 265-272, 2014.

64. P. Weisberg and Y. Wiseman, "Virtual Memory Systems Should Use Larger Pages rather than the Traditional 4KB Pages", International Journal of Hybrid Information Technology, Vol. 8(8), pp. 57-68, 2015.

65. Y. Wiseman, "Improved JPEG based GPS picture compression", Advanced Science and Technology Letters, Vol. 85, pp. 59-63, 2015.

66. Y. Wiseman, "Diminution of JPEG Error Effects", The Seventh International Conference on Future Generation Information Technology, Vol. 117, pp. 6-9, 2015.

67. Y. Wiseman, "Enhancement of JPEG Compression for GPS Images", International Journal of Multimedia and Ubiquitous Engineering, Vol. 10(7), pp. 255-264, 2015.

68. P. Weisberg and Y. Wiseman, "Virtual Memory Systems Should use Larger Pages", Advanced Science and Technology Letters, Vol. 106, pp. 1-4, 2015.

69. Y. Wiseman and Y. Giat, "Red Sea and Mediterranean Sea Land Bridge via Eilat", World Review of Intermodal Transportation Research, Vol. 5(4), pp. 353-368, 2015.

70. Y. Wiseman, "Alleviation of JPEG Inaccuracy Appearance", International Journal of Multimedia and Ubiquitous Engineering, Vol. 11(3), pp. 133-142, 2016.

71. Y. Wiseman, "Can Flight Data Recorder Memory Be Stored on the Cloud?", Journal of Aviation Technology and Engineering, Vol. 6(1), 16-24, 2016.

72. Y. Wiseman and I. Grinberg, "Autonomous Vehicles Should Not Collide Carelessly", Advanced Science and Technology Letters, Vol. 133, pp. 223-228, 2016.

73. Y. Wiseman and Y. Giat, "Multi-modal passenger security in Israel", Multimodal Security in Passenger and Freight Transportation: Frameworks and Policy Applications, Edward Elgar Publishing Limited, Chapter 16, pp. 246-260, 2016.

74. Y. Wiseman, "Traffic Light with Inductive Detector Loops and Diverse Time Periods", Contemporary Research Trend of IT Convergence Technology, Vol. 4, pp. 166-170, 2016.

75. Y. Wiseman, "Unlimited and Protected Memory for Flight Data Recorders", Aircraft Engineering and Aerospace Technology, Vol. 88(6), pp. 866-872, 2016.

76. Y. Wiseman and I. Grinberg, "When an Inescapable Accident of Autonomous Vehicles is Looming", International Journal of Control and Automation, Vol. 9(6), pp. 297-308, 2016.

77. Y. Wiseman, "Conceptual Design of Intelligent Traffic Light Controller", International Journal of Control and Automation, Vol. 9(7), pp. 251-262, 2016.

78. Y. Wiseman and I. Grinberg, "Circumspectly Crash of Autonomous Vehicles", Proc. IEEE International Conference on Electro Information Technology (EIT 2016), Grand Forks, North Dakota, USA, pp. 382-386, 2016.

79. Y. Wiseman, "Computerized Traffic Congestion Detection System", International Journal of Transportation and Logistics Management, Vol. 1(1), pp. 1-8, 2017.

80. Y. Wiseman, "Tool for Online Observing of Traffic Congestions", International Journal of Control and Automation, Vol. 10(6), pp. 27-34, 2017.

81. Y. Wiseman, "Safety Mechanism for SkyTran Tracks", International Journal of Control and Automation, Vol. 10(7), pp. 51-60, 2017.

82. Y. Wiseman, "Real-Time Monitoring of Traffic Congestions", IEEE International Conference on Electro Information Technology (EIT 2017), Lincoln, Nebraska, USA, pp. 501-505, 2017.

83. Y. Wiseman, "Automatic Alert System for Worn Out Pipes in Autonomous Vehicles", International Journal of Advanced Science and Technology, Vol. 107, pp. 73-84, 2017.

84. Y. Wiseman, "Vehicle Identification by OCR, RFID and Bluetooth for Toll Roads", International Journal of Control and Automation, Vol. 11(9), pp. 67-76, 2018.

85. Y. Wiseman, "Ancillary Ultrasonic Rangefinder for Autonomous Vehicles", International Journal of Security and its Applications, Vol. 12(5), pp. 49-58, 2018.

86. Y. Wiseman and I. Grinberg, "The Trolley Problem Version of Autonomous Vehicles", The Open Transportation Journal, Vol. 12, pp. 105-113, 2018.

87. Y. Wiseman, "In an Era of Autonomous Vehicles, Rails are Obsolete", International Journal of Control and Automation, Vol. 11(2), pp. 151-160, 2018.

88. Y. Wiseman, "Efficient Embedded Computing Component for Anti-Lock Braking System", International Journal of Control and Automation, Vol. 11(12), pp. 1-10, 2018.

89. Y. Wiseman, "Driverless Cars will Make Union Stations Obsolete", The Open Transportation Journal, Vol. 13, pp. 109-115, 2019.

90. Y. Wiseman, "Efficient Embedded Images in Portable Document Format (PDF)", International Journal of Advanced Science and Technology, Vol. 124, pp. 129-138, 2019.

91. Y. Wiseman, Israel Complementary International Airport, International Journal of Control and Automation, Vol. 12(7), pp. 1-10, 2019.

92. Y. Wiseman, "Driverless Cars will Make Passenger Rails Obsolete", IEEE Technology and Society, Vol. 38(2), pp. 22-27, 2019.

93. Y. Wiseman, "High Occupancy Vehicle Lanes are an Expected Failure", International Journal of Control and Automation, Vol. 12(11), pp. 21-32, 2019.

94. Y. Wiseman, "Rail Systems in Isolated Territories will Fade Away Once Autonomous Vehicles Emerge", Technical Report, 2020.

95. Y. Wiseman, "Blaumilch Canal on Ayalon Highway", Daaton, (2015), Available online at: http://www.daaton.co.il/Article.aspx?id=3290

96. Y. Wiseman, "Adjustable and Automatic Flush Toilet", Technical Report, 2020.

97. Y. Wiseman, "Autonomous Vehicles", Encyclopedia of Organizational Knowledge, Administration, and Technologies, First Edition, 2020.

98. M. Dreyfuss and Y. Giat, "Optimal spares allocation to an exchangeable-item repair system with tolerable wait", European Journal of Operational Research 261 (2), pp. 584-594, 2017.

99. Y. Giat, "The effects of output growth on preventive investment policy", American Journal of Operations Research 3 (06), pp. 474-486, 2013.